DIVISION 26 00 00					ELECTRICAL

SECTION 26 50 00 				LIGHTING

SECTION 26 56 00 				EXTERIOR LIGHTING

KNIGHT PEDESTRIAN LIGHTING

Part 1		General

- Summary

  - Section Includes:

    - Knight Pedestrian Lighting.

- Submittals

  - Provide submittals in accordance with Section 01 33 00 – Submittal Procedures.

  - Product data:

    - Manufacturer’s standard product literature.

    - Shop drawings.

    - Installation instructions.

    - Maintenance instructions.

  - Submit powdercoat finish samples for approval.

- Quality Assurance

  - Manufacturer Qualifications:

    - Minimum 15 years experience in the manufacture of outdoor lighting.

    - Provide reference list of at least ten major transportation authorities, municipalities, universities, or

other high-use public environments currently using outdoor lighting fabricated by the manufacturer.

- Delivery, Storage and Handling

  - Handle products in accordance with manufacturer’s instructions.

  - Store products in manufacturer’s original packaging until ready for installation.

  - Protect products from impacts and abrasion during storage.

- Warranty

  - Provide manufacturer’s standard warranty.

    - Warranty terms: three years from date of invoice against defects in materials and workmanship.

Part 2		Products

- Manufacturer

  - Basis-of-design product: provide pedestrian lighting fixture based on the product named.

    - Knight Pedestrian Lighting by Forms+Surfaces.

    - Manufacturer Contact:
Forms+Surfaces
30 Pine Street
Pittsburgh, PA 15223
phone: 800-451-0410

fax: 412-385-4715

email: sales@forms-surfaces.com

website: www.forms-surfaces.com

  - Pedestrian Lighting

    - Materials

      - Column: extruded aluminum with rounded corners.

      - Head: aluminum quadrant casting with aluminum lamp housing and four borosilicate glass lenses.

      - Driver:  Input power is 120-277 VAC, -30°C minimum starting temperature. Driver has 0-10V dimming capabilities. Certifications include: IP64 enclosure and Class 2 rated output (UL 8750).

      - LED light engine:

        - 60W custom LED light engine.

        - 4356 Luminaire Lumens

        - Color temperature (Select one color temperature below):

            - 3000K

            - 4000K

    - Finishes

      - Column and lamp housing: polyester powdercoat (Select one option below):

        - Standard Texture from Forms+Surfaces Powdercoat Chart.

        - Custom RAL powdercoat color.

      - Quadrant casting: “Forms+Surfaces Aluminum Texture” polyester powdercoat with polished outer edges. All surfaces are clear coated.

    - Dimensions

      - Overall: 6" square x 138" high.

    - Mounting: 3/8" thick stainless steel base plate, 5.50" square. Stainless steel mounting hardware sold separately. Template available upon request.

Part 3		Execution

- Examination

  - Verify that substrates are stable and capable of supporting the weight of items covered under this section.

  - Verify that substrates have been adequately prepared to securely anchor those items that will be surface

mounted.

- Installation

  - Install according to the manufacturer’s installation instructions.

  - Install in conformance to applicable ADA guidelines and End User’s established Accessibility policies.

END OF SECTION