DIVISION 12 00 00					FURNISHINGS

SECTION 12 93 00 				SITE FURNISHINGS

SECTION 12 93 23 				TRASH AND LITTER RECEPTORS

TRIAD RECEPTACLE

Part 1		General

- Summary

  - Section Includes:

    - 16-gallon triangular stainless steel with 6" diameter lid opening.

    - 16-gallon triangular stainless steel with 8" diameter lid opening.

    - 16-gallon triangular stainless steel with triangular lid opening.

    - 24-gallon trapezoidal stainless steel with 6" diameter lid opening.

    - 24-gallon trapezoidal stainless steel with trapezoidal lid opening.

    - 24-gallon trapezoidal stainless steel with paper slot lid opening.

- Submittals

  - Provide submittals in accordance with Section 01 33 00 – Submittal Procedures.

  - Product data:

    - Manufacturer’s standard product literature.

    - Shop drawings.

    - Installation instructions.

    - Maintenance instructions.

- Quality Assurance

  - Manufacturer Qualifications:

    - Minimum 15 years experience in the manufacture of litter and recycling receptacles.

    - Provide reference list of at least ten major transportation authorities, municipalities, universities, or

other high-use public environments currently using litter and recycling receptacles fabricated by the manufacturer.

- Delivery, Storage and Handling

  - Handle products in accordance with manufacturer’s instructions.

  - Store products in manufacturer’s original packaging until ready for installation.

  - Protect products from impacts and abrasion during storage.

- Warranty

  - Provide manufacturer’s standard warranty:

    - Warranty terms: three years from date of invoice against defects in materials and workmanship.

Part 2		Products

- Manufacturer

  - Basis-of-design product: provide receptacles based on the product named:

    - Triad Receptacle by Forms+Surfaces.

    - Manufacturer Contact:
Forms+Surfaces
30 Pine Street
Pittsburgh, PA 15223
phone: 800-451-0410

fax: 412-385-4715

email: sales@forms-surfaces.com

website: www.forms-surfaces.com

  - Receptacles

    - Materials:

      - Outer walls and base: stainless steel.

      - Lid: black polyethylene with UL94HB fire-rating.

      - Liners: black polyethylene with UL94HB fire-rating.

    - Finishes:

      - Outer walls (Choose one finish below):

        - Sandstone.

        - Linen.

        - Diamond.

        - Satin.

      - Lid (Choose one color below):

        - Black with a lightly textured finish.

        - Blue with a lightly textured finish.

        - Green with a lightly textured finish.

    - Dimensions (Select model(s) below):

      - 16-gallon, 6" diameter lid opening:

        - Overall: 18" wide per side x 15.5" deep x 32" high.

        - Nominal capacity: 16 gallons.

      - 16-gallon, 8" diameter lid opening:

        - Overall: 18" wide per side x 15.5" deep x 32" high.

        - Nominal capacity: 16 gallons.

      - 16-gallon, 9.5" opening per side, triangular lid opening:

        - Overall: 18" wide per side x 15.5" deep x 32" high.

        - Nominal capacity: 16 gallons.

      - 24-gallon, 6" diameter lid opening:

        - Overall: 23" wide x 15.5" deep x 32" high.

        - Nominal capacity: 24 gallons.

      - 24-gallon, 12.4" x 9.6" trapezoidal lid opening:

        - Overall: 23" wide x 15.5" deep x 32" high.

        - Nominal capacity: 24 gallons.

      - 24-gallon, 12.0" x 2.7" paper slot lid opening:

        - Overall: 23" wide x 15.5" deep x 32" high.

        - Nominal capacity: 24 gallons.

    - Instructional Graphics:

      - Apply instructional graphics to lids as specified to indicate the intended waste or recycling stream.

        - Graphics type: back-printed polycarbonate.

        - Letters and symbols color: White.

        - Graphics background colors:

            - Black.

            - Blue.

            - Green.

Installation (Select one below):

      - Freestanding: levelers included.

      - Surface mount: levelers included. Stainless steel anchors and mounting screws sold separately.

Part 3		Execution

- Examination

  - Verify that substrates are stable and capable of supporting the weight of items covered under this section.

  - Verify that substrates have been adequately prepared to securely anchor those items that will be surface

mounted.

- Installation

  - Install according to the manufacturer’s installation instructions.

  - Install in conformance to applicable ADA guidelines and End User’s established Accessibility policies.

END OF SECTION