DIVISION 26 00 00					ELECTRICAL

SECTION 26 50 00 				LIGHTING

SECTION 26 56 00 				EXTERIOR LIGHTING

TRIADA BOLLARD

Part 1		General

- Summary

  - Section Includes:

    - Illuminated bollard.

- Submittals

  - Provide submittals in accordance with Section 01 33 00 – Submittal Procedures.

  - Product data:

    - Manufacturer’s standard product literature.

    - Shop drawings.

    - Installation instructions.

    - Maintenance instructions.

  - Submit powdercoat finish samples for approval.

- Quality Assurance

  - Manufacturer Qualifications:

    - Minimum 15 years experience in the manufacture of outdoor lighting.

    - Provide reference list of at least ten major transportation authorities, municipalities, universities, or

other high-use public environments currently using outdoor lighting fabricated by the manufacturer.

- Delivery, Storage and Handling

  - Handle products in accordance with manufacturer’s instructions.

  - Store products in manufacturer’s original packaging until ready for installation.

  - Protect products from impacts and abrasion during storage.

- Warranty

  - Provide manufacturer’s standard warranty:

    - Warranty terms: three years from date of invoice against defects in materials and workmanship.

Part 2		Products

- Manufacturer

  - Basis-of-design product: provide bollards based on the product named:

    - Triada Bollard by Forms+Surfaces

    - Manufacturer Contact:
Forms+Surfaces
30 Pine Street
Pittsburgh, PA 15223
phone: 800-451-0410

fax: 412-385-4715

email: sales@forms-surfaces.com

website: www.forms-surfaces.com

  - Bollards:

    - Materials:

      - Body: one-piece contoured cast aluminum.

      - Head: three-part cast aluminum with frosted borosilicate glass cylinder, gasketed top and bottom.

      - Driver (LED lamps only): Input power is 90-305V, over-current and over-voltage auto recovery, -30°C starting temperature, IP66 (waterproof), Class A sound rating, and has 0-10V dimming capabilites.

      - Lamps (Choose one lamp option from below):

        - 34W LED 4000K.

            - Luminaire lumens: 620.

            - Color temperature: 4,000K.

        - 42W LED Amber.

            - Luminaire lumens: 676.

            - Color temperature: Amber.

    - Finishes: polyester powdercoat (Select one option below):

      - Standard Texture from Forms+Surfaces Powdercoat Chart.

      - Custom RAL Powdercoat color.

    - Dimensions:

      - Overall: 10.6" diameter x 41.9" high.

    - Mounting: surface mount with J-bolts, 1/4" thick aluminum base plate. Stainless steel mounting hardware sold separately. Templates available upon request.

Part 3		Execution

- Examination

  - Verify that substrates are stable and capable of supporting the weight of items covered under this section.

  - Verify that substrates have been adequately prepared to securely anchor those items that will be surface

mounted.

- Installation

  - Install according to the manufacturer’s installation instructions.

  - Install in conformance to applicable ADA guidelines and End User’s established accessibility policies.

END OF SECTION