SECTION 08 11 19

STAINLESS STEEL DOORS

Part 1		GENERAL

1.1	Summary

  - A.	Section Includes: Stainless steel doors with bead-blast etched decorative faces.

B.	Related Sections:

    - 03 30 00 – Cast-in-place concrete.

    - 04 20 00 – Unit masonry.

    - 06 20 00 – Finish carpentry.

    - 07 90 00 – Joint protection.

    - 08 06 10 – Door schedule.

    - 08 06 71 – Door hardware schedule.

    - 08 13 19 – Stainless steel doors.

    - 08 14 23 – Clad wood doors.

    - 08 34 00 – Special function doors.

    - 08 71 00 – Door hardware.

    - 08 80 00 – Glazing.

    - 09 20 00 – Plaster and gypsum board.

1.2	References

- A.	ANSI A250.4 - Test Procedure and Acceptance Criteria for Physical Endurance for Steel Doors and Hardware Reinforcing.

- ASTM A 167 - Stainless and Heat-Resisting Chromium-Nickel Steel Plate, Sheet, and Strip.

- NFPA 252 - Standard Methods of Fire Tests of Door Assemblies.

- AWS D9.1 - Sheet Metal Welding Code.

- NAAMM HMMA 860 - Guide Specifications for Hollow Metal Doors and Frames.

- NAAMM Metal Finishes Manual.

- SDI 100 - Recommended Specifications Standard Steel Doors and Frames.

1.3	Submittals

A.	Provide submittals in accordance with Section 01 33 00 – Submittal Procedures.

B.	Submit manufacturer’s shop drawings, installation drawings, installation instructions and maintenance instructions.

C.	Submit environmental impact data for all materials.

D.	Submit samples no less than 4" x 4" for all specified material finishes.

E.	Manufacturer information:

1.	Provide overview literature describing manufacturer’s overall scope of products and manufacturing capabilities.

2.	Provide URL for manufacturer’s website; website must provide access to technical data, images and general product information.

1.4	Quality Assurance

A.	Manufacturer Qualifications

1.	Minimum 10 years experience in the manufacture of architectural surface materials.

2.	Minimum 10 years experience in the fabrication of doors.

3.	Provide reference list of at least 10 public space projects currently using doors fabricated by the manufacturer.

B.	Installer Qualifications

1.	Minimum three years experience in the installation of doors.

1.5	Delivery, Storage and Handling

A.	Deliver materials to installation site in manufacturer’s original packaging. Handle products in accordance with manufacturer’s instructions. Store in dry, secure location, protected against direct sunlight and excessive heat. Protect finished surfaces with strippable film.

1.6	Warranty

A.	Provide manufacturer’s standard warranty.

1.	Warranty terms: one year against defects in materials and workmanship.

Part 2		PRODUCT

2.1	Manufacturer

A.	Provide Eco-Etch Doors by Forms+Surfaces,

Forms+Surfaces
30 Pine Street
Pittsburgh, PA 15223
phone: 800-451-0410

fax: 412-781-7840
email: sales@forms-surfaces.com

website: www.forms-surfaces.com

2.2	Door Type

A.	General

1.	Provide door faces with decorative designs applied by means of photolithographic bead-blast etching. Chemically etched designs not permitted.

B.	Decorative Face Material and Finish

1.	Stainless Steel Eco-Etch Doors

a.	Material: Stainless Steel

b.	Finish: Forms+Surfaces Seastone, Mirror, Satin (choose one)

c.	Eco-Etch pattern:	Forms+Surfaces City Lights, Current, Dash, Flicker, Glacier, Mica, Reeds, Seagrass, Sequence, Silkworm, Stacks, Stripe, Thatch, Trace, ECO202D, ECO204D, ECO205D, ECO208D (choose one)

2. Fused Metal® Doors

a.	Forms+Surfaces Fused Bronze, Fused Graphite, Fused Nickel Bronze, Fused Nickel Silver, Fused White Gold (choose one)

b.	Finish: Forms+Surfaces Seastone, Mirror, Satin (choose one)

c.  Eco-Etch pattern:	Forms+Surfaces City Lights, Current, Dash, Flicker, Glacier, Mica, Reeds, Seagrass, Sequence, Silkworm, Stacks, Stripe, Thatch, Trace, ECO202D, ECO204D, ECO205D, ECO208D (choose one)

  - Door Cores

  - Non-Rated

    - Provide wood core consisting of particleboard center section with a solid wood perimeter.

  - Fire-rated

    - Provide metal core with internal welded channel frame.

    - Core Material.

      - Depending on door size, application and required fire rating provide polystyrene, kraft honeycomb, temperature rise coreboard, steel stiffeners with fiberglass or mineral wool insulation or other core materials per referenced standards and applicable UL procedures.

2.4	Fire Rating

A.	General

1.	Provide assemblies labeled by Underwriters Laboratories complying with NFPA 80 and tested in accordance with ASTM E 152.

B.	Fire Rating

1.	Time: 3 hr, 1.5 hr, 1 hr, .75 hr, 20 min (choose one)

  - Neutral and Positive Pressure Ratings

    - Fire-rated doors shall conform to UL 10B for neutral pressure and UL 10C for positive pressure.

  - Temperature Rise Rating (TRR)

    - When required by Contract Documents, provide temperature rise rating down to 250º F @ 30 minutes

2.5	Edge Element

A.	Material: Clear, Black Anodized Aluminum (choose one)

2.6	Hardware Preparation and Supplied Hardware
A.		Hardware “Prep Only”

    - Per Contract Documents and approved drawings, provide doors with “prep only” for required hardware as specified. Hardware to be supplied by others.

  - Hardware “Prep-and-Supply”

    - Per Contract Documents and approved drawings, provide doors with “prep-and-supply” hardware package as specified.

  - Hardware Requirements for Fire-Rated Doors

    - Fire Rated doors must have the following minimum hardware:

      - Closer or spring hinges.

      - Automatic latching device (excludes roller latches and deadbolts) or concealed vertical rods.

      - Hinges or pivots.

      - Additional hardware may be added (deadbolts, viewers, flushbolts, door bottoms, etc).

      - All hardware must be UL listed and intended for use on fire-rated doors (positive and neutral pressure/UL10B & UL10C).

Part 3	EXECUTION

  - Examination

  - Verify that dimensions are correct and project conditions are suitable for installation. Do not proceed with installation until unsatisfactory conditions have been corrected.

  - Installation

- Install doors in accordance with manufacturer’s instructions, referenced standards and approved drawings.

- Ensure that doors are installed plumb and true, free of warp or twist, within tolerances specified in referenced standards and approved drawings.

- For fire-rated doors, verify that appropriate fire-rating labels are correctly applied to doors per referenced standards, Contract Documents, approved drawings and applicable UL procedures.

  - Adjust and Clean

- Test and verify correct operation of doors and related hardware. Adjust as needed.

- Clean doors in accordance with manufacturer’s instructions.